## Slide 1
Mapping Technology Overview
Philip Gershkovich
President
Cooper Aerial Surveys Co.
Copyright 2016

## Slide 2: Agenda
Overview
Ground Truth
Data Acquisition
GIS

## Slide 3: Ground Control
Notes: 3

## Slide 4: Aerial Target Control/Survey
Ground Control
  Surveyed to within 1/10 contour interval or better
  Basis/Datum?
  Verify elevations are ground elevations.
  Blind Panels
Digital Mapping Limits
  In control coordinates
  Corridor width
How long do panels last?
  Best Practice
Ground Truthing
Supplemental Topo
Notes: 4

## Slide 5: Remote Sensing
The acquisition, collection of information about the earth without making physical contact.
Photogrammetry – science of making measurements from photographs

## Slide 6: Work Flow Processes
Assess Needs
  Is aerial mapping/required
Project Scope
Flight
Aerial Triangulation
Compilation
Editing & QC
Ortho-Rectification

## Slide 7: Aerial Triangulation
Mathematical process used to determine the position and orientation of each photograph at the moment of exposure
  Image measurements to ground coordinates
  Critical step related to quality

## Slide 8: Survey Camera

## Slide 9: Flight

## Slide 10: Flight

## Slide 11: Flight Conditions
Roll, Pitch and Yaw
  Roll is the rotation about the
  y axis
  Pitch is the rotation about the
  x axis
  Yaw is the rotation about the z axis
Roll and Pitch is corrected by ABGPS
And IMU
The camera to be used must be equipped
with Forward Motion Compensation
(FMC) to Correct for Yaw.
The optical axis of the camera will be as near vertical as possible and in no case shall the tilt exceed 3 degrees. The tilt between two consecutive exposures shall not exceed 4 degrees.

## Slide 12: Flight Conditions Cont.
Time of day for flight will be when shadows caused by topographic relief, and sun angle will be near minimum, and at low tide. Excessive and deep shadows may be cause for rejection of photography. Sun angle shall not be less than 40 degrees.
The aerial Photography will be acquired under leaf-off conditions and will take place in November to December to achieve these results.

## Slide 13: Drones

## Slide 15: 2D Data
Remote Sensed Imagery
Planimetrics

## Slide 16
RGB
NIR

## Slide 17: 3D Data
Digital Surface Model
Digital Terrain Model
Triangulated Irregular Network
Orthorectified Imagery
Contours
LiDAR

## Slide 18: LiDAR
Analyzing
Multiple Features:
  Man-made
  Geographic
  Vegetation
Notes: 18

## Slide 20: Processing
Pixel to point cloud
  Photos are now converted to point clouds which function similarly as LiDAR data

## Slide 22: Photogrammetry vs. LiDAR
Notes: 22
Key Model Point Blowup

## Slide 23
Photogrammetry vs. LiDAR

## Slide 24
LIDAR Video

## Slide 25: LiDAR Products
Pros
  Can be less expensive than photogrammetry
  Deliveries in a shorter time frame
  Minimal Ground Control without truthing
  Good solution when no access for ground control
  Good data in vegetated areas
Cons
  Planimetrics are challenging
  10-20 times more data
  May contain anomalies
  No minor break detail
  Not a smooth surface

## Slide 26: Questions?
Notes: 26

## Slide 27: Thank you very much!
Email with any questions:
  Zachary Radel (Sr. Project Manager)
    zachary@cooperaerial.com
  Philip Gershkovich (President)
    phil@cooperaerial.com
    WWW.COOPERAERIAL.COM
Notes: 27